## Slide 1
Can we achieve multi-spectral consistency in retrievals and simulations of clouds and precipitation?
Identifiy EarthCARE/GPM coincidences
Run latest ACM-CAP EarthCARE retrieval assimilating MSI solar/thermal channels
Run Tco1279 IFS with extra diagnostics (12-24 h forecasts)
Use RTTOV to simulate GPM microwave channels (10-183 GHz), MSI thermal and solar channels, BBR fluxes and BBR radiances, from ACM-CAP and IFS
Use ZmVar to simulate EarthCARE reflectivity
Robin Hogan, Emma Turner, Shannon Mason, Mark Fielding
Thanks to Shunsuke Aoki for the EarthCARE/GPM coincidence database!

## Slide 2: Tropical Cyclone Bheki (Indian Ocean) 18 Nov 2024 (Cat 4)
VIIRS NOAA-21: 09:13
GPM rain rate (used in IMERG): 09:00
EarthCARE overpass: 09:14
GPM
EarthCARE

## Slide 3: Tropical Cyclone Bheki (Indian Ocean) 18 Nov 2024
IFS rain rate (50 mm/h) is excellent!
ACM-CAP underestimates peak rain rate by a factor of 10

## Slide 4: TC Bheki
ACM-CAP retrieved ice treated as cloud ice in RTTOV
Rain-sensitive 10 GHz BT underestimated
ZmVar with IFS microphysics predicts strong attenuation but no multiple scattering
ACM-CAP simulates broadband fluxes very well
Ice-sensitive high frequencies not well captured either
Rain-sensitive 10-GHz BT well captured
Ice-sensitive high frequencies better than ACM-CAP but not perfect

## Slide 5: TC Bheki
ACM-CAP retrieved ice treated as snow in RTTOV
Need to run with ACM-CAP’s assumptions!
Rain-sensitive 10 GHz BT underestimated
ZmVar with ACM-CAP microphysics (Field/SSRGA) looks much better!
ACM-CAP simulates broadband fluxes very well
Ice-sensitive high frequencies well captured!
Rain-sensitive 10-GHz BT well captured
Ice-sensitive high frequencies better than ACM-CAP but not perfect

## Slide 6: TC Bheki
ACM-CAP forward-models radiances: good agreement
Tripleclouds slightly higher than delta-Eddington: representing heterogeneity
Split-window difference well captured
RTTOV DOM with Baran optics not quite right
RTTOV MFASIS higher than DOM with Baran optics
RTTOV can model broadband radiance but underestimates clear sky
Baran optics

## Slide 7: TC Bheki
Baum optics
ACM-CAP forward-models radiances: good agreement
Tripleclouds slightly higher than delta-Eddington: representing heterogeneity
Split-window difference well captured
RTTOV DOM with “Baum” optics much better (liquid effective radius also used)
RTTOV MFASIS closer to DOM with Baum ice optics
RTTOV broadband radiances improved;
still underestimates clear sky

## Slide 8: Next steps
This is one case: I’ve run the IFS for 165 more in many different conditions, and Emma has simulated 8 so far
How can we improve ACM-CAP rain retrievals? 94-GHz path-integrated attenuation is well predicted so is there too much liquid cloud in rain assumed?
Use ice particle scattering assumptions in ACM-CAP to do proper high frequency closure in microwave
Resolve differences in solar: DOM vs MFASIS vs FLOTSAM?
Tripleclouds quite close to delta-Eddington in infrared, but how do we adapt to the microwave where sub-grid inhomogeneity of precipitation is important?
How can we improve the assumptions in the IFS for assimilating all wavelengths?
Hoping to get an ESA-ECMWF Fellow to take this work further in 2027 preparation for the FORUM far-infrared Earth Explorer mission

## Slide 9: Pre-Tropical Storm Hector (NE Pacific) 22 August 2024
VIIRS NOAA-20: 21:10
GPM rain rate: 21:46
EarthCARE overpass: 21:51
GPM
EarthCARE
Gilma
Pre-Hector

## Slide 10: Pre-Hector
GPM retrieves peak rain rate of around 8 mm/h along EarthCARE track
ACM-CAP underestimates rain rate by a factor of 2 rather than 10!
IFS system too wide and weak

## Slide 11: Pre-Hector
ACM-CAP retrieved ice treated as cloud ice in RTTOV
Rain-sensitive 10 GHz BT underestimated
Peak reflectivity underestimated, cloud water has higher reflectivity than rain!
ACM-CAP simulates broadband fluxes very well
Ice-sensitive high frequencies not well captured either
System too broad and weak at all frequencies

## Slide 12: Pre-Hector
ACM-CAP retrieved ice treated as snow in RTTOV
Rain-sensitive 10 GHz BT underestimated
ACM-CAP settings look better, but not enough attenuation in rain
ACM-CAP simulates broadband fluxes very well
Ice-sensitive very well captured!
System too broad and weak at all frequencies

## Slide 13: Pre-Hector
ACM-CAP forward model overestimates infrared split-window difference
RTTOV uses Baum ice: excellent agreement