## Slide 1: Towards using EarthCARE and GPM to improve radiance models, retrievals and microphysical understanding
Robin J. Hogan, Emma Turner, Shannon Mason, Mark Fielding & Kamil Mroz (ECMWF)
Thanks to Shunsuke Aoki (JAXA) & Leonhard Scheck (LMU)

## Slide 2: Overview
What can we learn from coincident observations by EarthCARE and GPM?
  Wavelengths span 5 orders of magnitude: passive from 0.6 mm to 3 cm, active from 0.3 mm to 2.2 cm
In this talk we forward-model GPM observations, using as input both EarthCARE synergy retrievals (ACM-CAP) and ECMWF weather forecasts (IFS)
  Crucial test of RTTOV radiance model used in assimilation, recently updated to calculate radar profiles
  Are our ice microphysical and scattering assumptions capable of spanning this wavelength range?
  How good are EarthCARE’s rain retrievals? Can we increase the upper limit on retrieved rain rate?
  How can we use this information to improve processes in weather and climate models?
This is work in progress!

## Slide 3: Data flow in this talk…
EarthCARE
EarthCARE
GPM
Test BE baseline of ACM-CAP, radiative closure using BBR
Test weather forecasts using same models
RTTOV used for assimilating radiances, recently able to simulate radar profiles as well
ZmVar used for assimilating CPR and soon ATLID at ECMWF
CPR radar
MSI imager
BBR radiances
ATLID lidar
ACM-CAP retrieval
ECMWF IFS model
RTTOV satellite simulator
ecRad radiation scheme
ZmVar radar simulator
CPR radar
MSI imager
BBR fluxes
DPR
radar
GMI imager
Multiple satellite radiances, including GPM’s GMI
ACM-CAP forward models
Observations
Atmospheric properties
Radiative transfer schemes
Simulated obs.

## Slide 4: Pre-Tropical Storm Hector (NE Pacific) 22 August 2024
VIIRS NOAA-20: 21:10
GPM rain rate: 21:46
EarthCARE overpass: 21:51
GPM
EarthCARE
02698E
Gilma
Pre-Hector
GMI
IFS

## Slide 5: Forward-modelled radiances
IFS
EarthCARE
10 GHz
36 GHz
89 GHz
165 GHz
Shortwave
Longwave
Poor ZmVar simulation using IFS microphysical assumptions
Storm system too broad and weak
Treat ACM-CAP ice as cloud ice in RTTOV
Rain-sensitive radiances are too low
Ice-sensitive radiances are too high
Broadband fluxes well captured

## Slide 6: …improved ice assumptions
IFS
EarthCARE
10 GHz
36 GHz
89 GHz
165 GHz
Shortwave
Longwave
Better ZmVar simulation using ACM-CAP microphysical assumptions!
Storm system too broad and weak
Treat ACM-CAP ice as snow in RTTOV
Rain-sensitive radiances are too low
Ice-sensitive radiances are much better
Broadband fluxes well captured

## Slide 7
a
ACM-CAP rain rate agrees well with GPM’s 2A DPR product, but but both less than its 2A GMI “GPROF” product!
Forward modelled 35.5 GHz: reflectivity profile excellent, PIA underestimated
13.6 GHz
35.5 GHz
94 GHz
Measured
ACM-CAP
RTTOV
IFS
RTTOV
PIA
Profiles
✓
?

## Slide 8: Tropical Cyclone Bheki (Indian Ocean) 18 Nov 2024 (Cat 4)
VIIRS NOAA-21: 09:13
GPM rain rate (used in IMERG): 09:00
EarthCARE overpass: 09:14
GPM
EarthCARE
01337E
GMI
IFS
50 mm/h

## Slide 9: Bheki: forward-modelled radiances
IFS
EarthCARE
10 GHz
36 GHz
89 GHz
165 GHz
Shortwave
Longwave
Rain-sensitive radiances much too low with ACM-CAP, about right with IFS
Ice-sensitive radiances are well captured
Broadband fluxes well captured
✓
✗
✓

## Slide 10: Potential to improve EarthCARE retrievals of heavy rain?
IFS simulates the rain intensity well!
ACM-CAP ice water path too high: 20 kg m-3
PIA saturates at 65-85 dB, corresponding to a rain rate of around 5 mm/h: ACM-CAP needs to be able to distinguish “saturated PIA” from “missing PIA” and use in retrievals
ACM-CAP snow flux just above melting layer is a bit better: can we extend it down into the rain?
Possible improvement: assume denser ice when multiple scattering diagnosed, leading to less IWP but potentially higher ice mass flux, and feed this into rain retrieval below?

## Slide 11: Cirrus and boundary-layer cloud (SE Pacific) 13 Feburary 2026
VIIRS NOAA-21: 18:41
GPM rain rate: 18:56
EarthCARE overpass: 18:59
GPM
EarthCARE
04058F
210 K
330 K
Infrared brightness temperature

## Slide 12: Low cloud & cirrus: radiances
IFS
EarthCARE
10 GHz
36 GHz
89 GHz
165 GHz
Shortwave
Longwave
35/89 GHz radiances in low clouds agree well
ACM-CAP predicts a larger scattering signal in 89/165 GHz channels than observed by GMI

## Slide 13: Comparison of retrievals
Rain rate -40°N to -34°N:
  GMI: 0.012 mm/h
  ACM-CAP: 0.013 mm/h
  IFS: 0.020 mm/h
Liquid water path
  GMI: 84 g m-3
  ACM-CAP: 105 g m-3
  IFS: 36 g m-3
IWP -46°N to -42°N:
  GMI: 4.9 g m-3
  ACM-CAP: 395 g m-3
  IFS: 254 g m-3
GMI barely detects cirrus?
GMI and ACM-CAP agree well in low cloud but much finer scale from EarthCARE
IFS: too much rain from too little cloud
÷100!

## Slide 14: Outlook
Huge potential to use EarthCARE/GPM coincidences to improve ice & rain size distribution and scattering assumptions, and to improve retrievals
Next steps:
  Ensure microwave forward models in RTTOV use consistent ice scattering model as retrieval, and provide constraints on ice size distributions and density
  Understand differences in size distributions between warm and cold rain, reconciling raindrop number/size retrievals and making use of Doppler velocity
  Can we bridge the gap between mid-infrared and microwave to obtain consistent ice optical properties in the far-infrared in preparation for FORUM?
Other ideas:
  Can we assimilate EarthCARE’s PIA? Tight constraint on rain rate
  EarthCARE II should carry a suite of microwave radiometers!

## Slide 16: CPR brightness temperature

## Slide 17: Pre-Hector: Comparing Nw
Normalized number concentration from GPM 2B synergy retrieval and from EarthCARE’s ACM-CAP